## Slide 1: Hall Effect Sensors
Jayden Marcom (Team 5)

## Slide 2: What Are Hall Effect Sensors
Makes use of the Hall Effect
Magnetic field Sensor

## Slide 3: What is the Hall Effect
Edwin Herbert Hall in 1879
Repeated experiment by Henry Augustus Rowland
Gold leaf
Electromagnets

## Slide 4: Understanding the Hall Effect
Begin with a current flowing through a conductor. Then place it within a magnetic field.

## Slide 5: Understanding the Hall Effect
Lorentz Force
Electric force from charge buildup
Pushes Electrons/Protons to one side

## Slide 6: Composition of Hall Effect Sensors
Gallium Arsenide, Indium Arsenide, or Indium Antimonide
Dc amplifier
Input, Output, and ground Leads

## Slide 7: Uses of Hall Effect Sensors
Hall Effect sensors are used in a variety of products (bicycles, phones, keyboards, etc.)
Speed Sensors
Pressure Sensors
Current Sensors
Magnetic Field Sensors

## Slide 8: How to use a Hall Effect Sensor
Effective Range
Voltage Range
Type of Hall Effect Sensor

## Slide 9: Types of Hall Effect Sensors
Typically designed to turn on
Digital or Linear(analog) outputs
Bipolar or Unipolar
Specialization in sideways vs head-on

## Slide 10: Voltage Range of Hall Effect Sensor
Choice of range
Digital or Analog
Cutting of the voltage range

## Slide 11: Effective Range of Hall Effect Sensor
Gauss rating of sensor(1 Telsa = 10,000 Gauss)
Magnet size or distance
Apply an appropriate formula

## Slide 12: Formula for Square/Rectangle magnets
B is the B field in Gauss.
is the remanence field or residual induction (These can be found in the magnet datasheet).
z is the distance from the pole face of the magnet.*
L is length of the magnet*.
W is the width of the magnet*.
D is the thickness/height of the magnet*
*Units do not matter(all the same)

## Slide 13: Formula for Disc/Rod magnets
B is the B field in Gauss.
is the remanence field or residual induction (These can be found in the magnet datasheet).
z is the distance from the pole face of the magnet.*
R is radius of the magnet.*
D is the thickness/height of the magnet*.
*Units do not matter(all the same)

## Slide 14: Formula for Ring Magnets
B is the B field in Gauss.
is the remanence field or residual induction (These can be found in the magnet datasheet).
z is the distance from the pole face of the magnet.*
is the outer radius of the magnet.*
is the inner radius of the magnet.*
D is the thickness/height of the magnet*.
*Units do not matter(all the same)

## Slide 15: Formula for Sphere Magnets
B is the B field in Gauss.
is the remanence field or residual induction (These can be found in the magnet datasheet).
z is the distance from the pole face of the magnet.*
R is the radius of the magnet.*
D is the thickness/height of the magnet*.
*Units do not matter(all the same)

## Slide 16: Conclusion

## Slide 17: References
http://hyperphysics.phy-astr.gsu.edu/hbase/magnetic/Hall.html
The discovery of the Hall effect, G S LEADSTONE, Physics Department, Atlantic College, South Wales
https://www.electronics-tutorials.ws/electromagnetism/hall-effect.html
https://www.supermagnete.de/eng/faq/How-do-you-calculate-the-magnetic-flux-density